## Slide 1: Team 16 Knuckles, The Assistive Robotic Arm Andrew Blanchard (Team Leader), Matthew van Zuilekom, Rym Benchaabane, Paola Hernandez
ECE 4336: ECE Design II
Faculty: Dr. Dmitri Litvinov
Faculty Advisor: Dr. Becker
Sponsored by IEEE UH Makers
Friday, April 26th 2019
Notes: Andrew

## Slide 2: Overall Project
What is Knuckles?
  Stationary, 3D printed voice activated assistive robotic arm that will hand the user objects and tools upon request
  Home robot
Purpose
  Assist those who are limited in physical capacity
  Decrease the risk of dexterity incidents
  Increase the user’s productivity
Examples of users
  Elderly
  People with disabilities
  Lab researchers
Notes: Andrew

## Slide 3: Overview Diagram
Figure 1. Overview of Knuckles functionalities
Notes: Andrew

## Slide 4: Related Patents
Patent 1: US 10,242,334 B2
Machine Readable Delivery Platform for automated package delivery
Patent 2: 8,077,963 B2
Mobile robot with a head-based movement mapping scheme
Patent 3: 10,223,732 B2
Identifying Items in Images
Figure 2. Knuckles holding a phone
Our project will not be patented but will be open-source.

## Slide 5: Design Considerations
Starting point:
  BCN3D Moveo, open-source 3D-print design from a 3D printing company in Barcelona that was based off another robot built for a Hack-a-day project
Project is a proof-of-concept, not an alpha prototype
Notes: Matthew

## Slide 6: Design Considerations
Figure 3. Modular Diagram of Knuckles system
Notes: Matthew:
24V/12V converters: Step down 120VAC to 24VDC and 12VDC. 24V connects to larger motors, 12V connects to smaller motors.
Connect to 120V mains: Home robot. Connection to 120VAC mains allows Knuckles to be used in any home.
Chose Tb6560 instead of original BOM stepper motor drivers to accommodate overheating system and centralize wires/cables. Also the stepper drivers have 3 axises each, so we only needed to use 2 stepper drivers.
Arduino microcontroller + RAMPS 1.4V: Easily program motor control, RAMPS 1.4V as a shield to protect arduino against high voltage.
BOM was also available, we modified to accommodate our specs

## Slide 7: Design Considerations
Figure 6. Knuckles in default position
Figure 4. Microphone & 3D-printed cased Raspberry Pi 3B+
Figure 5. Tb6560 Stepper drivers
Wooden base and 3D printed cases to protect equipment
Ring shaped taps to better wire routing
Two Tb6560 instead of six (BOM)

## Slide 8: Design Constraints
Overheating motors. Needed a larger base motor
  Current divider using switches on stepper drivers
Two-finger gripper reduces grab capabilities
  Limited objects to grab
Limited range of reach (0.5 m)
  Stationary robot
Notes: Paola

## Slide 9: Design Constraints
Link 5
Link 4
Link 3
Link 2
Link 1
Link | Length (cm) | Part and Motors Mass (kg) | Total Torque (N.m)
5 | 17.5 | 0.849 | 0.110
4 | 12.6 | 0.690 | 0.216
3 | 22.2 | 0.640 | 2.08
2 | 22.2 | 3.20 | 6.00
1 | 16.8 | 1.00 | 0.710
Table 1. Torque calculations to choose motors
Goal: maximum weight rating = 0.5 kg
Figure 7. Knuckles in upright position
Notes: 3.6 N.m

## Slide 10: Deliverables
FALL 2018 | WINTER BREAK | SPRING 2019
Assembling: Physical arm and gripper prototype 1 (100%) | Assembling: Tune gripper and arm motors motion (90%) | User Interface: Develop a Graphic User Interface (QTdesigner)
Hardware Purchased: (Intel RealSense camera, Intel mic, tactile pads) (100%) | Hardware Implementation Mount and install on Arm (Intel RealSense camera, Intel mic, tactile pads) (50%) | Automation Control: Arm moves using data from ROS (50%)
Object Detection: Recognize the AprilTag and associate it to an object (100%) | Object Detection: Arm follows the AprilTag (90%) | Voice Recognition: Convert voice to speech speech to object detection (15%)
Simulation: Arm functions on RViz (100%) | Communication System: Receive Feedback Signals from all hardware on ROS (100%) | Physical arm Prototype 2
Table 2. Expected deliverables from Fall semester
Notes: Andrew

## Slide 11: Deliverables
 | SPRING 2019
Assembling: Tune gripper and arm motors motion (100%) | User Interface: Develop a Graphic User Interface (QTdesigner) (85%)
Hardware Implementation Mount and install on Arm (Intel RealSense camera, Intel mic) (100%) | Automation Control: Arm moves using data from ROS (100%)
Object Detection: Arm follows AprilTag (100%) | Voice Recognition: Convert voice to speech speech to object detection (100%)
Communication System: Receive Feedback Signals from all hardware on ROS (100%) | Physical Arm Final Build: (100%)
SPRING 2019
Table 3. Deliverables at the end of Spring semester

## Slide 12
Prototypes & Schedule
LEGEND
Deadlines
Prototype Demo
Prototypes
1
3
2
ECEDHA Conference
Delay
Figure 8. Gantt Chart
Notes: Converted Knuckles from prototype to proof-of-concept.
-started in June. Had to learn EVERYTHING from scratch Machine learning. Removed since Apriltags are hard-coded
Object detection with OpenCV and Tensorflow. Replaced with Apriltags.
-Face recognition. Creating own voice recognition, so Knuckles would find the user
Depth camera. Removed since Apriltags provide distance. This is why we got RealSense
UR3. Was not provided so we had to build Moveo.
Touch sensors. Object can be pulled away from Knuckles easily
Multidirectional microphone. Originally planned to have Knuckles point towards the user

## Slide 13: Test Plan
Robotic Arm:
  Test each motor (link) with pulleys (6 links total)
  Test gripper with different objects
AprilTag Detection:
  Test for correct tag distance, orientation and ID on Rviz and ROS
  Test for text commands on ROS
Voice Commands:
  Test for correct voice command on Raspberry Pi3+
  Test for communication system with PubNub and ROS
GUI:
  Test if text commands, camera and error display matches ROS and Rviz

## Slide 14: Specifications
Degrees of Freedom (DOF) Arm – Five
Accuracy Voice Interpretation – 95%
Minimum Voltage for Motors – 12V
Object Detection – AprilTags
Object Count Library – 9
Response phrases - 64
Response Time – 7 seconds
Maximum Grabbing Reach – 0.5 meter
Maximum Weight Rating – 0.5 kg
Notes: Paola

## Slide 15: Features
Powered by Mains – Yes
Integrated Microphone – Yes
Integrated Camera – Yes
Object Detection with AprilTags
Voice-Controlled using Alexa Voice Service – Yes
User-Friendly GUI – Yes
Wi-Fi required – Yes
Notes: Paola

## Slide 16
Graphical User Interface (GUI)
Figure 9. Knuckles graphical user interface
Notes: Paola

## Slide 17: Risk Management Matrix
Probability
Consequence
Figure 10. Risk management matrix
Damage during shipping
Unexpected risk
Notes: Matthew

## Slide 18: Risk Mitigation
GUI fail to communicate with Knuckles
  Use speech-to-text
No internet connection available, Alexa voice detection unavailable
  Use text input instead of voice
3D parts melting due to motor heat
  Re-print melted parts and/or replace motors
Stepper drivers shorting
  Have four extra stepper drivers as replacements
Arduino or Raspberry Pi become faulty due to burnt connections
  Get replacements at Library Makerspace
Damaged arm due to shipping packaging*
  Reprint damaged parts
Notes: Matthew

## Slide 19: Conclusion Thank you IEEE UH Makers, Dr. Roysam & Dr. Becker!
Summary
  Proof-of-concept
  Assistive robotic arm, increase productivity
  Great opportunity to learn about robotics, Linux & ROS
Future works
  Implementation of object detection and recognition
  Enhancement of position awareness using limiters and encoders
  Conversion of Knuckles to a mobile robot to expand uses
  Upgrade Knuckles' gripper to adapt to a wider range of object shapes
  Improvements on searching methods for user using the multi-directional microphone
Lessons learned
  Systems integration, verification and testing
  Risks management and patent search
  Delegate tasks based on individual skill-set
Notes: Paola

## Slide 20: Thank you for your attention!
QUESTIONS OR COMMENTS?
Notes: Yay

## Slide 21: References: Voice Commands
From Workspace to Knuckles
"Pick up"
From Workspace to User
"Hand me"
"Give me"
"Bring me"
"Get me"
From Knuckles to Workspace
"Put Down"
From Knuckles to User
"Release"
"Let Go"
From User to Knuckles
"Take"
"Grab"
"Hold"
Knuckles Settings
"Scan for objects"
"Go Upright"
"Go Down"
"Default"
"Stop"
"That it recovered"
"Forget saved objects"
"Restart"
Knuckles activates with: "Alexa trigger Knuckles to"
Objects aka April Tags
"Apple"
"Bottle"
"Wallet"
"Phone"
"Box"
"Tape"
"Cup"
"Bag of Chips"
“User”