## Slide 1
Introduction
Problem: People are rushed and tend to multitask. According to the scientific journal, Current Biology, attempting to multitask reduces productivity by around 40%. SMF Mutual Insurance adds that multitasking can lead to dexterity incidents while performing hands-on work.
Need: A tool that will help the user multitask, increase productivity and avoid dexterity incidents.
Purpose
A stationary, 3D-printed, voice activated, assistive robotic arm that will retrieve items within its workspace upon request. It is designed to assist those who are limited in physical or in task capacity while also being able to increase overall productivity.
Knuckles, The Assistive Robotic Arm
Andrew Blanchard, Matthew van Zuilekom, Rym Benchaabane, Paola Hernandez Sponsored by IEEE UH Makers
UH Makers
Specifications
Degrees of Freedom (DOF) Arm – 5
Accuracy Voice Interpretation – 95%
Minimum Voltage for Motors – 12 [V]
Object Detection – AprilTags
Object Count Library – 8 items
Response phrases – 64
Response Time – 7 [s]
Maximum Grabbing Reach – 0.5 [m]
Maximum Weight Rating – 0.5 [kg]
Features
Powered by Mains: 120 [VAC]
Integrated Microphone
Integrated Camera
Voice-Controlled using Alexa Voice Service
Object Detection with AprilTags
User-friendly GUI
Wi-Fi required
Acknowledgements Our team would like to thank Dr. Roysam,
Dr. Becker, Dr. Trombetta, Dr. Litvinov, Rhema Ike, George Godinez, Yang Nguyen & Aaron Hollaway for their advice and valuable contribution.
Figure 4: Left: Knuckles in upright position
Right: Knuckles in default position
Conclusions
Impact: Proof of concept for a voice controlled home robotics and automation system to assist users with physical limitations in completing common tasks.
Future work:
Implementation of object detection and recognition.
Enhancement of position awareness using limiters and encoders.
Conversion of Knuckles to a mobile robot to expand uses.
Upgrade Knuckles' gripper to adapt to a wider range of object shapes.
Improvements on searching methods for user using the multi-directional microphone.
Design Considerations
Voice Input
  Multi-directional Microphone: Allows user to be heard from anywhere within room
  Alexa Voice Service: Convert voice-to-text without developing a voice recognition library
Camera Input
  RealSense Camera: Small lightweight camera
  AprilTags: Tags provide the translation, distance, and orientation with respect to the camera instead of using an object detection algorithm
Power System
  120 [VAC] Mains: Knuckles can easily be plugged in anywhere
  24 [V]/12[V] Converters: Provides 24 [V]/12[V] to stepper motors drivers
Graphical User Interface
  User-friendly Interface: Monitors Knuckles’ status and program updates
Figure 2: Graphical User Interface
Figure 1: Overview diagram of Knuckles’ functionalities
Figure 3: Voice input processing block-diagram
Voice Input
Intel Speech Enabling Development Kit
(Microphone)
Raspberry Pi 3 B+
Amazon Alexa Voice Service
IFTTT (Alexa Skill)
Webhook PubNub
ROS
Digital Signal of Input
Digitized Voice Input
Wi-Fi
Speech-to-Text
Text Command
Design Limitations
Maximum lift weight – 0.5 [kg]
Fixed number of detectable objects – 8
Limited grip capabilities
Short range of reach – 0.5 [m]
Non-mobile robot